## Slide 1
Digital Dash
Portland State University
Department of Electrical and Computer Engineering (ECE)
Sean Koppenhafer, Jaime Rodriguez,
Chad Thueson, Noah Erickson, Rishal Dass
Project Proposal
Notes: 1
1

## Slide 2
Overview
Project Overview & Requirements
Devices Chosen
  Microcontroller
  CAN Transceiver
  LCD Screen
GUI Layout
Enclosure
Budget
Project Timeline
Notes: 2
2

## Slide 3: Project Overview
Electric systems add complexity and a traditional LED dash won't suffice
Drivers must be aware of system faults and warnings
An LCD Dashboard must be created to accommodate additional electrical systems
Formula SAE Electric Car
Current Traditional LED Dash

## Slide 4: Project Requirements
Budget: $500
Timeline: March 2015
The display gather information from the CAN-bus and display it in a simple LCD GUI
Deliverables
  One functional Unit
  Well Documented Code
  Professional Documentation
  User Manual

## Slide 5: Design Constraints
Choose most suitable LCD display
Design the communication interface with VCU
Develop GUI
Design waterproof casing for the display
Physical space on dash is limited

## Slide 6
Devices Chosen
CAN Protocol for data acquisition with serial to LCD
AT90CAN Atmel
AMS-42700 On Semiconductor
uLCD-35DT 4D systems
Notes: 6

## Slide 7
Microcontrollers
 | Cost | Fab Board | CAN Controller | CAN Library | SPI, I2C, UART, etc
Atmega 328 | ~$3 | Yes | No | No | Yes
AT90CAN | ~$8 | Yes | Yes | Yes | Yes
Arduino Uno | ~$25 | No | No | No | Yes
Arduino Due | ~$50 | No | Yes | No | Yes
Notes: 7

## Slide 8
CAN Transceiver
 | Cost | Max Transfer Rate | Multiple CAN networks
AMIS-42700 | ~$6 | 1 Mbit/sec | Yes (2 networks)
MCP-2551 | ~$1.50 | 1 Mbit/sec | No (1 network)
Notes: 8

## Slide 9
Reasons for Choices
CAN is the standard for vehicle communication
Low message transfer latency
Simplicity to implement and expand
Other options
  Serial
  Wireless
  USB
Notes: 9

## Slide 10
LCD Screen
2.7” LCD display 3.5” LCD display
4.7” LCD display (too large)
Pros
  Resistive Touch
  Color display
  Power Graphics processor
  Simple tools to create Gui
  High Resolution
Cons
  Screen is not polarized, difficult to see in sunlight (shield can be bought)
P/N uLCD-35DT
Notes: 10

## Slide 11
GUI Layout
Proposed - Display GUI Layout (basic)
Battery meter will indicate voltages between safe and critical levels.
Flashing warnings symbols will indicate errors in BMS, and IMD System.
Temperature indicator for motor or controller.

## Slide 12
GUI Layout
Notes: 12

## Slide 13
Enclosure
On top of dash
Pros
  Looks good
Cons
  3D Printed (expensive)
  Sticks out of cockpit (rule violation?)
In Dash
Pros
  Looks good
  Waterproof
Cons
  3D Printed (expensive)
  Limited View
Notes: 13
13

## Slide 14
Budget
AT90CAN ~$10, plus ~$20 for board FAB
4D 3.5" Screen ~$150 for screen & shield
Deutsch Connectors ~$10
Enclosure ~$50
$250 for one system
Notes: 14

## Slide 15
Project Timeline
Notes: 15

## Slide 16
Questions & Concerns?
Notes: 16