Viking Motorsports
Digital Dash
Project Requirements
January 3rd, 2015

Sean Koppenhoffer, Rishal Dass
Jaime Rodriquez, Noah Erickson, Chad Thueson

Background

Objective

The digital dash will give the operator of the electric car critical system warnings of various systems. The warnings will come from a CAN bus connected from the electric car VCU that will be connected to a microcontroller contained in the digital dash unit. The microcontroller will parse the CAN data and display it on the LCD contained in the digital dash unit. The microctonroller, LCD and a power supply will be contained in a waterproof enclosure that is easily installable on to the current setup of the Formula SAE electric car.

Constraints

The LCD display must be readable in all weather conditions. A trans-reflective display that is 500-900 nits bright will allow the display to be readable in sunlight. A waterproof enclosure will allow the device to operate in rainy conditions and allow it to be readable in rain. The digital dash unit must be large enough to be readable but small enough to be mountable on the dash of the electric car. A 3.5” LCD screen will allow for both size constraints.

Standards

The digital dash unit must adhere to the Formula SAE rules. The main article here is that the digital dash must be contained inside the cockpit of the electric car.